## Slide 1: GNU Programski alati

## Slide 2: Proces prevođenja programa
Komandom
  gcc –save-temps -hello.c –o hello
  Pokreće se proces prevođenja izvornog C programa u izvršni program na mašinskom jeziku (save temps opcija ne briše radne fajlove procesa).
Proces obuhvata faze makroprocesiranja, kompajliranja (prevođenja), asembliranja i povezivanja
gcc je compiler driver koji orkestrira pojedine alate

## Slide 3: Proces prevođenja programa
hello.c
#include <stdio.h>
#define PORUKA "Zdravo svete.\n"
main() {
printf(PORUKA);
}

## Slide 4: Proces prevođenja programa
Faza makroprocesiranja. Pretprocesor (cpp) menja originalni C program prema direktivama koje počinju # znakom.
Na primer, #include komanda u liniji 1 hello.c govori pretprocesoru da pročita sadržaj sistemskog stdio.h zaglavlja datoteke i ubaci ga direktno u programski tekst.
#define vrši zamenu makroimena PORUKA tekstom zamene “Zdravo svete.”
Rezultat je još jedan C program hello.i
(Eksplicitan poziv: cpp hello.c –o hello.i)

## Slide 5: Proces prevođenja programa
hello.i
# 1 "hello.c"
# 1 "/usr/arm-linux-gnueabi/include/stdio.h" 1 3 4
. . . .
extern int printf (__const char *__restrict __format, ...);
. . . .
# 2 "hello.c" 2
main() {
printf("Zdravo svete.\n");
}

## Slide 6: Proces prevođenja programa
Faza kompilacije. Prevodilac (cc1) prevodi tekst datoteke hello.i u tekstualni fajl hello.s, koji sadrži program u asemblerskom jeziku.
Svaka naredba asemblerskog programa opisuje jednu naredbu u mašinskom jeziku. Asemblerski jezik je zajednički izlaz za različite kompajlere (na primer, C kompajler i Fortran kompajler).
Direktan poziv:
gcc -print-prog-name=cc1
/usr/lib/gcc/arm-linux-gnueabi/4.6/cc1
/usr/lib/gcc/arm-linux-gnueabi/4.6/cc1 hello.i –o hello.s

## Slide 7: Proces prevođenja programa
hello.s
.cpu arm10tdmi
.fpu softvfp
. . .
.file "hello.i"
.section .rodata
.align 2
.LC0:
.ascii "Zdravo svete.\000"
.text
.align 2
.global main
.type main, %function
main:
@ args = 0, pretend = 0, frame = 0
@ frame_needed = 1, uses_anonymous_args = 0
stmfd sp!, {fp, lr}
add fp, sp, #4
ldr r0, .L2
bl puts
mov r0, r3
ldmfd sp!, {fp, pc}
.L3:
.align 2
.L2:
.word .LC0
.size main, .-main
.ident "GCC: (Ubuntu/Linaro 4.6.3-1ubuntu5) 4.6.3"
.section .note.GNU-stack,"",%progbits

## Slide 8: Proces prevođenja programa
Faza asembliranja. Asembler (as) prevodi hello.s u mašinski jezik, pakuje ga u obliku poznatom kao relokativni objektni program i čuva rezultat u hello.o objektnoj datoteci. Hello.o fajl je binarni fajl koji pored bajtova mašinskih instrukcija čuva još informacije o globalnim simbolima itd.
Direktno pozivanje: as hello.s -o hello.o
file hello.o
hello.o: ELF 32-bit LSB relocatable, ARM, version 1 (SYSV), not stripped

## Slide 9: Proces prevođenja programa

## Slide 10: Proces prevođenja programa
$ arm-linux-gnueabi-objdump -f -t -d hello.o
(objdump prikazuje imformacije o objektnim i izvršnim fajlovima
–f hederi, -t simboli, -d disasembler)
hello.o: file format elf32-littlearm
architecture: arm, flags 0x00000011:
HAS_RELOC, HAS_SYMS
start address 0x00000000
SYMBOL TABLE:
00000000 l df *ABS* 00000000 hello.i
00000000 l d .text 00000000 .text
00000000 l d .data 00000000 .data
00000000 l d .bss 00000000 .bss
00000000 l d .rodata 00000000 .rodata
00000000 l d .note.GNU-stack 00000000 .note.GNU-stack
00000000 l d .comment 00000000 .comment
00000000 l d .ARM.attributes 00000000 .ARM.attributes
00000000 g F .text 0000001c main
00000000 *UND* 00000000 puts
Disassembly of section .text:
00000000 <main>:
0: e92d4800 push {fp, lr}
4: e28db004 add fp, sp, #4
8: e59f0008 ldr r0, [pc, #8] ; 18 <main+0x18>
c: ebfffffe bl 0 <puts>
10: e1a00003 mov r0, r3
14: e8bd8800 pop {fp, pc}
18: 00000000 .word 0x00000000
hello.o

## Slide 11: Proces prevođenja programa
Faza povezivanja. Primetiti da program hello poziva printf funkciju, koja je deo standardne C biblioteke koje pruža svaki C kompajler.
printf funkcija nalazi se u posebnom pretkompajliranom objektnom fajlu pod nazivom printf.o, koji mora nekako da se spoji sa našim hello.o programom.
Linker (ld) obavlja ovo povezivanje. Rezultat je hello fajl, koji je izvršni objektni fajl (ili jednostavno izvršni fajl) koji je spreman da se učita u memoriju i izvršava od strane operativnog sistema.

## Slide 12: Proces prevođenja programa
Faza povezivanja. Da bismo znali kako tačno pozvati linker (ld) korisno je zadati verbose opciju gcc -v hello.c –o hello koja ispisuje kako prednji kraj poziva svaki alat (collect2 je fasada za ld):
. . . .
/usr/lib/gcc/arm-linux-gnueabi/4.6/cc1 -quiet -v -imultilib . -imultiarch arm-linux-gnueabi hello.c -quiet -dumpbase hello.c -march=armv7-a -mfloat-abi=softfp -mfpu=vfpv3-d16 -mthumb -auxbase hello -version -fstack-protector -o /tmp/ccABMJ6E.s
. . . .
/usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/bin/as -march=armv7-a -mfloat-abi=softfp -mfpu=vfpv3-d16 -meabi=5 -o /tmp/ccfgZLdU.o /tmp/ccABMJ6E.s
. . . .
/usr/lib/gcc/arm-linux-gnueabi/4.6/collect2 --build-id --no-add-needed --as-needed --eh-frame-hdr -dynamic-linker /lib/ld-linux.so.3 -X --hash-style=gnu -m armelf_linux_eabi -z relro -o hello /usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/lib/../lib/crt1.o /usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/lib/../lib/crti.o /usr/lib/gcc/arm-linux-gnueabi/4.6/crtbegin.o -L/usr/lib/gcc/arm-linux-gnueabi/4.6 -L/usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/lib/../lib -L/usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/lib -L/lib/arm-linux-gnueabi -L/usr/lib/arm-linux-gnueabi -L/usr/lib -L/lib /tmp/ccfgZLdU.o -lgcc --as-needed -lgcc_s --no-as-needed -lc -lgcc --as-needed -lgcc_s --no-as-needed /usr/lib/gcc/arm-linux-gnueabi/4.6/crtend.o /usr/lib/gcc/arm-linux-gnueabi/4.6/../../../../arm-linux-gnueabi/lib/../lib/crtn.o

## Slide 13: Proces prevođenja programa
Faza povezivanja
Na komandnoj liniji linkera (ld) redosled zadavanja fajlova je sledeći:
crt1.o crti.o crtbegin.o [-L paths] [user objects] [gcc libs] [C libs] [gcc libs] crtend.o crtn.o
Informativno objašnjenje crt (c run time) fajlova koji daju podršku izvršavanju prevedenog C programa. To su male sekcije koda koje se ubacuju (ld) i izvršavaju na početku prevedenog C programa i na kraju. Ovaj kod se brine za inicijalizaciju globalnih promenjljivih, heap-a i steka:
crt0.o Older style of the initial runtime code. Usually not generated anymore with Linux toolchains, but often found in bare metal toolchains. Serves same purpose as crt1.o (see below).

## Slide 14: Proces prevođenja programa
crt1.o Newer style of the initial runtime code. Contains the _start symbol which sets up the env with argc/argv/libc _init/libc _fini before jumping to the libc main. glibc calls this file 'start.S'.
crti.o Defines the function prolog; _init in the .init section and _fini in the .fini section. glibc calls this 'initfini.c'.
crtn.o Defines the function epilog. glibc calls this 'initfini.c'.
Scrt1.o Used in place of crt1.o when generating Position Independent Executables (PIEs).
gcrt1.o Used in place of crt1.o when generating code with profiling information. Compile with -pg. Produces output suitable for the gprof util.
Mcrt1.o Like gcrt1.o, but is used with the prof utility. glibc installs this as a dummy file as it's useless on linux systems.

## Slide 15: Proces prevođenja programa
crtbegin.o GCC uses this to find the start of the constructors.
crtbeginS.o Used in place of crtbegin.o when generating shared objects/PIEs.
crtbeginT.o Used in place of crtbegin.o when generating static executables.
crtend.o GCC uses this to find the start of the destructors.
crtendS.o Used in place of crtend.o when generating shared objects/PIEs.

## Slide 16: Proces prevođenja programa
Faza povezivanja.
Statičko povezivanje (sav bibliotečki kod biće ubačen u izvršni fajl):
  export L=/usr/arm-linux-gnueabi/lib
  export L1=/usr/lib/gcc/arm-linux-gnueabi/4.6
  arm-linux-gnueabi-ld -L$L1 -static $L/crt1.o $L/crti.o $L1/crtbeginT.o hello.o -lc -lgcc -lgcc_eh $L1/crtend.o $L/crtn.o -o shello
crt1.o…

## Slide 17: Proces prevođenja programa
Faza povezivanja.
Dinamičko povezivanje (dinamički povezivač će u trenutku startovanja povezati kod našeg programa sa deljenom bibliotekom):
  export L=/usr/arm-linux-gnueabi/lib
  export L1=/usr/lib/gcc/arm-linux-gnueabi/4.6
  arm-linux-gnueabi-ld -dynamic-linker /lib/ld-linux.so.3 $L/crt1.o $L/crti.o $L1/crtbegin.o hello.o -lc $L1/crtend.o $L/crtn.o -o hello

## Slide 18: Proces prevođenja programa
Dinamičko povezivanje
U TRENUTKU IZVRŠAVANJA PROGRAMA

## Slide 19: Proces prevođenja programa
Statičko vs dinamičko povezivanje – veličina izvršnog programa:
$ ls –l *
-rwxrwxr-x 1 bb bb 4848 Mar 3 18:02 hello
-rw------- 1 bb bb 83 Mar 2 06:29 hello.c
-rw------- 1 bb bb 19011 Mar 2 06:38 hello.i
-rw------- 1 bb bb 1036 Mar 2 07:43 hello.o
-rw------- 1 bb bb 692 Mar 2 07:32 hello.s
-rw------- 1 bb bb 8552 Mar 2 08:12 hello.txt
-rwxrwxr-x 1 bb bb 452397 Mar 3 18:17 shello

## Slide 20: Proces prevođenja programa
hello: file format elf32-littlearm
architecture: arm, flags 0x00000112:
EXEC_P, HAS_SYMS, D_PAGED
start address 0x00008311
SYMBOL TABLE:
. . . .
Disassembly of section .init:
000082bc <_init>:
82bc: b508 push {r3, lr}
82be: f000 f843 bl 8348 <call_gmon_start>
82c2: bf00 nop
82c4: bd08 pop {r3, pc}
. . . .
Disassembly of section .text:
00008310 <_start>:
8310: f04f 0b00 mov.w fp, #0
8314: f04f 0e00 mov.w lr, #0
. . .
00008388 <main>:
8388: b580 push {r7, lr}
838a: af00 add r7, sp, #0
838c: f248 30f0 movw r0, #33776 ; 0x83f0
8390: f2c0 0000 movt r0, #0
8394: f7ff efa2 blx 82dc <_init+0x20>
8398: 4618 mov r0, r3
839a: bd80 pop {r7, pc}
Disassembly of section .fini:
000083e4 <_fini>:
83e4: b508 push {r3, lr}
83e6: bf00 nop
83e8: bd08 pop {r3, pc}